## Slide 1: Navigating the e-fuel landscape: demand drivers, cost and willingness to pay
A Market Report by Aurora Energy Research
February 2025

## Slide 2: Our E-fuels Report offers an in-depth view of the European e-fuel market development, cost drivers and acceleration factors for uptake
In Aurora’s Report Navigating the e-fuel landscape, we answer the most important questions on cost, market and pricing dynamics of four key e-fuels: Ammonia, Methanol, e-Kerosene and e-Methane. These include:
    Is European production of e-fuels competitive in the face of international imports?
    What are the most promising e-fuels?
    How do costs change under different business models for e-fuel producers?
    How large is the gap between levelised cost of production and the willingness to pay?
    What will determine the competitive advantage of e-fuel producers in Europe?
    How can the ‘missing money’ gap be closed?
    With the Report you receive a supporting data book and one 2-hour sessions with the authors of the report and other hydrogen experts to discuss the findings.
Credentials
Aurora has extensive experience across the entire hydrogen value chain and is well placed to provide in-depth analysis of e-fuels and their role in Europe’s decarbonisation journey.
Throughout Europe we have advised utilities, financial institutions and asset owners on the supply and demand dynamics of the emerging hydrogen market.
Aurora’s price outlooks are regularly tested by a large subscriber base when it comes to financing investment decisions.
We are delighted to offer this in-depth Report to you.
Source: Aurora Energy Research
A 2-hour session with the authors of the Report to discuss the results
Expert session
Report
140 Powerpoint slide in pdf format
Including all key inputs and outputs of the analysis in the Report
Excel data book
Notes: We want to convince them to join the MCS
Content
Clients present along the value chain. You will be sitting with a group of clients who will be with a bunch of people who are really good at this.
Clients may not be familiar with what MCS is
  For a small fee you can join the multi client study

## Slide 3
Executive summary 9 slides
Fundamentals 32 slides
  Policy framework
  Key e-fuels and value chains
  Use cases and key competing technologies
Cost of production 25 slides
  Fundamentals and plant setup
  Levelised cost of e-fuels
  Economic assumptions
  Cost comparison
Supply and demand dynamics 28 slides
  Potential market size
  Supply mix
Willingness to pay for e-fuels 25 slides
  Overview
  Deep dive: maritime sector
Sensitivity: levelised cost of e-fuels 12 slides
Acceleration factors: regulatory push and pull factors 9 slides

## Slide 4: The EU’s Fit for 55 package is the main policy and regulatory driver for the development of the e-fuel sector
Sources: Aurora Energy Research, European Commission
1) Renewable fuel of non-biological origin, include renewable hydrogen and its derivatives. 2) The reform under “Fit for 55” reduces the number of allowances on the market and increases funding for decarbonisation. 3) Commission Delegated Regulations (EU) 2023/1184 and (EU) 2023/1185.
II. Fundamentals – 1. Policy framework
Following the climate targets set in the Paris Agreement, the European Council and the European Commission established the European Green Deal in 2019, setting out the EU‘s climate strategy. A policy framework has been constructed to implement the Green Deal, and many parts of which engage with the e-fuel industry.
Frameworks
Renewable Energy Directive (RED) III RFNBO1 targets
The overall EU target for renewable energy sources consumption by 2030.
ReFuelEU aviation
Mandates that aims to reduce aviation's carbon emissions by increasing the use of sustainable aviation fuels.
FuelEU maritime
Mandates that aims to reduce greenhouse gas emissions from the shipping industry.
Alternative Fuels Infrastructure Regulation (AFIR)
Targets that aims to allow for an easier use, more reliable, and more accessible charge and refuel of vehicles and ships with alternative fuels.
Combustible car ban from 2035, e-fuel exemption
In 2023, the EU agreed to ban the sale of new combustion engine cars from 2035 onwards, except for cars that run exclusively on e-fuels.
EU Emissions Trading System (ETS) Reform2
The system puts a price on carbon. Every year, entities covered by the ETS have to buy “allowances” corresponding to their emissions.
EU Carbon Border Adjustment Mechanism (EU CBAM)
Tool to put a fair price on the carbon emitted during the production of carbon intensive goods that are entering the EU.
Innovation Fund
Fund aimed at delivering the commitments under the Paris Agreement and the climate and energy priorities set by policy packages.
RED III regulatory framework
The Renewable Energy Directive3 is the legal framework for the development of clean energy across all sectors of the EU economy.
Direct e-fuel policy frameworks
Indirect e-fuel policy frameworks
E-fuel regulatory framework
Deep-dive
1
Deep-dive
2
Deep-dive
3
Example page from Report (redacted)

## Slide 5: Hydrogen costs are heavily depending on the country, where grid usage allows for significantly lower costs
Chart: 
 | 8.7 | 10.9 | 8.4 | 7.1
 | 10.9 | 8.6 | 7.1 | 6.3
 | 8.6 | 7.9 | 5.7 | 5.1
 | 4.8 | 4.6 | 4 | 3.5
 | 3.4133 | 3.2 | 2.6311 | 2.2756
 | 4.6933 | 4.4 | 3.6178 | 3.1289
 | 4.3733 | 4.1 | 3.3711 | 2.9156
For all countries, the electrolyser has a ratio of 2:1 between power source and electrolyser with an optimal mix of renewable capacities.
For all European countries, the PPA-based LCOH is used, as the plant is assumed to be close to an industrial site or CO2 source, which does not allow for co-location of renewables.
Brazil, Australia and Qatar are assumed to use co-location of the electrolyser with renewables for the hydrogen production.
Green hydrogen cost (LCOH) for different COD years, PEM electrolyser €/XX (real 2023)
Country 1
Country 2
Country 3
Country 4
Country 5
Country 6
Country 7
Sources: Aurora Energy Research
III. Cost of production – 3. Economic assumptions
Example page from Report (redacted)
Redacted
Notes: Not the most optimal power procurement strategy, e.g., no grid use for Spain for the 2030 price
Germany increase because of no exemption from grid fees from 2030 onwards
Italy is higher because of high grid fees

## Slide 6: E-kerosene remains significantly more expensive compared to fossil fuel
Chart: 
 | 4289.123 | 3739.5732 | 3471.7985 | 2234.178 | 2351.4781 | 2153.0902 | 1759.1558 | 515.4545
 | 22.9502 | 14.6047 | 13.0399 | 288
Country 1
Country 2
Country 3
Country 4
Country 5
Country 6
Country 7
Benchmark
Benchmark
Germany, Italy, and Spain have the highest e-kerosene cost due to high hydrogen production costs.
Australia is on a similar cost level as Sweden, Brazil can offer the lowest e-kerosene cost.
Nevertheless, the low-cost hydrogen countries, such as Sweden, Australia, Qatar, and Brazil cannot compete with the fossil kerosene price due to high hydrogen and CO2 demand for production.
Transport costs only increase the final costs slightly, as it is liquid under atmospheric conditions and large existing infrastructure exists.
Levelised cost of e-kerosene in 2030 and benchmark €/XXX (real 2023)
Sources: Aurora Energy Research, International Air Transport Association
III. Cost of production – 4. Cost comparison
Chart: 
 | 1
 | 1
 | 1
Levelised cost of e-fuel
Import cost
CO2 cost
Redacted
Example page from Report (redacted)
Notes: - No country gets near the

## Slide 7: E-fuel potential market size is XXX by 2030 and XXX by 2050
Sources: Aurora Energy Research
1) The EU e-fuel potential market sizing is calculated for the 27 European Union countries.
IV. Supply and demand dynamics - 1. Potential market size
Final energy consumption, energy use, by “e-fuel relevant” sectors in the EU1
Unit
2030
2050
Chart: 
 | 160771.7412 | 1344.4508 | 93491.454 | 55137.115 | 55137.115
 | 8021.7999 | 0 | 7894.9356 | 0 | 254263.1952
 | 0 | 0 | 0 | 4191.2514 | 20107.9868
 | 0 | 0 | 0 | 0 | 1344.4508
E-ammonia
E-kerosene
E-methanol
E-methane
Total e-fuel
Use case 1
Use case 2
Use case 3
Use case 4
Chart: 
 | 286829.3486 | 568991.976 | 166796.0591 | 76950.5813 | 76950.5813
 | 94427.168 | 0 | 90352.3309 | 0 | 453625.4077
 | 0 | 0 | 0 | 48306.9427 | 233086.4416
 | 0 | 0 | 0 | 0 | 568991.976
E-ammonia
E-kerosene
E-methanol
E-methane
Total e-fuel
Example page from Report (redacted)
Redacted
Redacted
Notes: How we built the demand section
2030 is mainly from existing industries
2050 is mainly from aviation

## Slide 8: E-fuel floor WtP accounts for current grey fuel prices, avoided penalties related to carbon costs and quota non-compliance
Sources: Aurora Energy Research
V. Willingness to pay for e-fuels - 1. Overview
Illustrative levelised floor WtP1 for RFNBO e-fuels, EU (COD 2030) €/kg (real 2023)
. |  |  |  |  |  | 
Chart: 
 | 2.6917 | 2.6917 | 3.8689 | 6.2233 | 6.7233 | 6.7233 | 7.7233
 | 1.1772 | 2.3544 | 0.5 | 1
Price of grey fuel
Carbon costs
Avoided penalties - non-compliance
Subsidies
Floor WtP
Required green premium
LCOe-fuel
1) WtP: Willingness to pay.
Price of grey fuel
Carbon costs
Avoided penalties - non-compliance
Subsidies
Floor WtP
Required green premium
LCOe-fuel
Deep-dive
1
Deep-dive
2
Deep-dive
3
Deep-dive
4
Example page from Report (redacted)
Redacted
Redacted
Redacted
Redacted
Redacted
Redacted
Redacted
Notes: Methodology slides
What is included in Floor WtP
What is green premiums

## Slide 9: Aurora has constructed a high cost and low cost project set-up sensitivity on the LCOe-fuel
Base scenario
Sources: Aurora Energy Research
VI. Sensitivity: levelised cost of e-fuels
Space restrictions do not allow for co-location of electrolyser or carbon capture.
Requires hydrogen purchase agreement (HPA).
Requires pipeline transport of hydrogen and CO2.
No retrofitting of brownfield production site possible for e-ammonia and e-methanol.
Expensive industrial CO2 in all countries.
A tight PPA market leads to increased PPA prices, varying by country.
Excellent location allows for additional co-location with renewable assets.
Reduced grid fees in all countries and 13k mechanism in Germany.
Optimal hydrogen procurement strategy.
Usage of grid power when possible during lifetime.
Large oversizing of PPA possible.
Reduced electrolyser CAPEX.
Sufficient supply of biogenic CO2 in all countries.
Low cost scenario
High cost scenario
Carbon capture
Electro-lyser
E-fuel plant
Renewables/grid
Carbon capture
Electro-lyser
E-fuel plant
Renewables/grid
A good location allows for co-location with electrolyser and carbon capture.
Space restrictions do not allow for co-location of renewable assets.
Retrofitting of brownfield production site possible for e-ammonia and e-methanol.
Cheap industrial CO2 available until 2041, afterwards biogenic sources only in Germany and Sweden, while in Spain and Italy DAC.
Carbon capture
Electro-lyser
E-fuel plant
Pipeline
Pipeline
Co-location
Co-location
PPA
PPA
Co-location/ PPA/Grid
Co-location
Co-location
On site
On site
On site
Renewables/grid
Redacted
Redacted
Redacted
Example page from Report (redacted)
Notes: Start in the middle with a recap on the base case
High cost case including factors that drive up costs, both project setup and external (political/market) factors
Low cost scenario includes factors that improve project setup and external factors

## Slide 10: Bridging the gap between WtP and LCOe-fuel will require a combination of policy and regulatory push and pull factors
Sources: Aurora Energy Research
VII. Acceleration factors: push and pull
Illustrative cost and WtP1 for RFNBO e-fuels €/kg (real 2023)
Chart: 
 | 1 | 1 | 1.3 | 2.5 | 2.8 | 2.8 | 3.4 | 4 | 4.3
 | 0.3 | 1.2 | 0.3 | 0.6 | 0.6 | 0.3
WtP
RED III and penalties
e-fuel offtake subsidies
CCfDs
Balanced price
Grid fee reduction
Hydrogen
Carbon
LCOe-fuel
1) Willingness to pay.
WtP
Push factors
Final price
Pull factors
LCOe-fuel
Deep-dive
1
Deep-dive
2
Deep-dive
3
Deep-dive
4
Deep-dive
5
Estimated impact
on LCOe-fuel
Estimated impact
on WtP
XX%
XX%
XX%
XX%
XX%
XX%
Push factors
Pull factors
Redacted
Example page from Report (redacted)
Notes: Methodology slides
What is included in Floor WtP
What is green premiums

## Slide 11
Add a pricing slide with different options:
Report alone: 30k
Report with expert session: 35k
Report with expert session and data add on: 40k

## Slide 12: Contact the authors of the report and experts who have contributed to address any questions
Frederik Beelitz Frederik.Beelitz@auroraer.com | David Olley David.Olley@auroraer.com | Emma Keisser Emma.Keisser@auroraer.com | Emma Woodward Emma.Woodward@auroraer.com | Kevin Caballero Henkel
Advisory Principal | Senior Associate | Associate | European Hydrogen Market Lead | 
Leads Aurora’s Central Europe Advisory hydrogen and decarbonisation practice | Specialised in hydrogen markets, flexible energy, and auction design | Specialised in H2 projects at Aurora, with a background in infrastructure asset management | Advises on all aspects of the development of a hydrogen economy in Europe | 
Source: Aurora Energy Research
Kevin to add picture, email and short bio